## Slide 1
QuadruJuggle — Hierarchical Control Architecture
Ball Sensor
Camera / depth raw pos (noisy)
Kalman Filter
position + velocity estimation @ 200 Hz
noisy pos
Pi1 — High-Level Planner (choose one)
Mirror Law
Analytic geometry n̂ = norm(v_out/e − v_in) roll/pitch → 6D cmd (zero training needed)
OR
Learned Pi1 (RL)
PPO policy 46D obs → 6D cmd apex curriculum [0.10–0.60 m]
Hybrid Switch: Pi1 builds energy → Mirror Law holds height
ball state (46D obs)
Pi2 — Torso Tracker (frozen)
Pre-trained RL policy | 6D torso cmd → 12D joint targets | ~200M steps, never retrained
6D torso cmd (h, ḣ, roll, pitch, vx, vy)
Go1 Robot
12-DOF quadruped PD control @ 200 Hz custom paddle attachment
12D joint targets
Ball
m = 50 g | e = 0.85 physical bouncing
paddle impulse
← ball trajectory (sensed)
✓ analytic — no training
trained: PPO ~570M steps
trained: PPO ~200M steps — shared by all Pi1 variants